## Slide 1
Learnable Nonlinear Circuitry in Printed Neuromorphic Computing System
Master Thesis
Zhidong Yang, Supervisor: Haibin Zhao
Notes: thanks for your introduction

## Slide 2: Background
Learnable Nonlinear Circuitry in Printed Neuromorphics
Introduction of printed Neuromorphics
Neuromorphic Computing
    inspired by the workings of the brain, neural network(NN)
    simple primitive operations: weighted-sum & activation function
    high ability to approximate desired functionalities
Printed electronics (PE)
    Flexibility:High level customization due to additive manufacturing
    nontoxicity, ultra low-cost…
Notes: This work is based on printed Neuromorphics. Printed Neuromorphics(use printed electronics to
Implement Neuromorphic Computing), so how to
,

## Slide 3: Background
Learnable Nonlinear Circuitry in Printed Neuromorphics
weigthed-sum
Crossbar work as weighted-sum
    weighted-sum:
    crossbar :
    where , and
crossbar for weighted-sum

## Slide 4: Background
Learnable Nonlinear Circuitry in Printed Neuromorphics
Activation function
Nonlinear Circuit as activation function
    where is the auxiliary parameter, which
    describe the form of this characteristic curve.

## Slide 5: Background
Learnable Nonlinear Circuitry in Printed Neuromorphics
Printed Neural Network (pNN)
Printed Neural Network (pNN)
  ML-based model for design of printed neuromorphic circuits
  Learnable parameter in pNN
  Training a pNN w.r.t. is designing a printed neuromorphic circuit
Notes: With these circuits, To design of printed neuromorphic circuits

## Slide 6: Motivation
Learnable Nonlinear Circuitry in Printed Neuromorphics
Realted work
Previous works
  only in crossbar (weight in NN) are learnable
  nonlinear circuit(activation function in NN) are always predefined
  high customization provided by PE is not leveraged
This work
  make the nonlinear circuit learnable (learnable activation function)
    the components (include of nonlinear circuit are also learnable
  the training of pNNs for learnable nonlinear circuit

## Slide 7: Methodology
Learnable Nonlinear Circuitry in Printed Neuromorphics
Differentiable model for learnable nonlinear circuit
  NN-based Approximator
Integrate NN-based Approximator into pNNs for learnable activation function
The training for pNNs
  considering variation-aware training and learning flexibility
Notes: To do this,

## Slide 8: Differentiable model for learnable nonlinear circuit
Learnable Nonlinear Circuitry in Printed Neuromorphics
Parameters
  Learnable: physical quantities
  Activation function: auxiliary parameter
Differentiable map fromto by NN
Notes: What does model do for leanable, learnable, function of learnable

## Slide 9: Pipeline for modeling of nonlinear circuit
Learnable Nonlinear Circuitry in Printed Neuromorphics
Design space & constraints
Draw 10000 sets of physical quantities with Quasi Monte-Carlo sampling
Pipeline for modeling of nonlinear circuit
Notes: Sensitivity analysis

## Slide 10: Pipeline for modeling of nonlinear circuit
Learnable Nonlinear Circuitry in Printed Neuromorphics
For each sample we do the simulation of nonlinear circuit(green points)
We fit the points with tanh and auxiliary parameter
Train a NN (NN-based Approximator) with input and output
Notes: Sensitivity analysis

## Slide 11: NN-based Approximator
Learnable Nonlinear Circuitry in Printed Neuromorphics
Training of Approximator
  Data preprocessing
    extend input firstly
    normalize and to and secondly
  Data split: train(70%)/valid(20%)/test(10%) set
  Hyperparameter tuning regarding #layer, learning rate
resulted Approximator
  15 layer
  learning rate 0.01
Analysis
  acceptable prediction compared to true value
  no overfitting problem during the training
Notes: Validloss, extend first. integration, the physical quantities are optimizable. Moreover, the variation of these physical quantities values are caused by fabrication errors, so we can also consider the fabrication error of these physical quantities in the training

## Slide 12: Variation-aware Training
Learnable Nonlinear Circuitry in Printed Neuromorphics
Taking fabrication error/variation into account
Model the learnable parameter as stochastic variables, e.g.,
  with each element in and following a uniform distribution in this work
  , reflects printing technology
  build activation/negative weight functions
  in pNNs
Notes: \epsilon
Loss. Only an approximate solution through numerical methods. Monte/Carlo approximation.
objective existence

## Slide 13: Learning flexibility
Learnable Nonlinear Circuitry in Printed Neuromorphics
Different learning flexibility :
    neuron-level: each neuron has independent learnable activation function
    layer-level: the same learnable activation function are shared by all neurons in a layer
    net-level: the same leanable activation function are shared across all neurons
Experiment for learning flexibility
  13 benchmark datasets
  Data split: train(60%)/valid(20%)/test(20%) set
  Data preprocessing: normalization
  Topology: #input – 3 – #output
  Seeds ∈{0, …, 9}
.
Input
Output
Hidden layer
Notes: To decide which learning flexibility is applied in the final experiments.

## Slide 14: Results for learning flexibility
Learnable Nonlinear Circuitry in Printed Neuromorphics
The mean and standard deviation from valid set under different training frameworks
  Despite the higher number of learnable parameters, the pNNs with neuron-level and layer-level do not perform significantly better than the pNNs with net-level
  The training of pNNs with net-level is also time-saving.
.
Notes: For different datasets, the performance of different learning flexibility can be better than else.
To demonstrate the results from different datasets more intuitively, we average the accuracies and standard deviation over all datasets as a scalar
So we use net-level in the final experients

## Slide 15: Experiment for learnable nonlinear circuit
Learnable Nonlinear Circuitry in Printed Neuromorphics
-
13 benchmark datasets
Data split: train(60%)/valid(20%)/test(20%) set
Data preprocessing: normalization
topology: #input – 3 – #output
Seeds ∈{0, …, 9}
Assumption without variation (nominal training)
  nonlearnable nonlinear circuit
  learnable nonlinear circuit
.

## Slide 16: Results
Learnable Nonlinear Circuitry in Printed Neuromorphics
4.2% accuracy improvement
Notes: We pick the best model with minimum valid loss, and evaluate it with test sets

## Slide 17: Experiment for variation-aware training
Learnable Nonlinear Circuitry in Printed Neuromorphics
-
13 benchmark datasets
Data split: train(60%)/valid(20%)/test(20%) set
Data preprocessing: normalization
topology: #input – 3 – #output
Seeds
With learnable nonlinear circuit
  nominal training
  variation-aware training
Variation
  5% and 10% in test
.

## Slide 18: Results under 5% variation in test
Learnable Nonlinear Circuitry in Printed Neuromorphics
Analysis: compare to nominal training,
  10.7% Accuracy and 84.8% Robustness(standard deviation) improvement
.

## Slide 19: Results under 10% variation in test
Learnable Nonlinear Circuitry in Printed Neuromorphics
Analysis: compare to nominal training,
  19.2% Accuracy and 75.5% Robustness improvement
.

## Slide 20: Conclusion
Learnable Nonlinear Circuitry in Printed Neuromorphics
-
Enable bespoke implementation of nonlinear circuit in printed neuromorphic circuits for individual tasks
  Build model(NN-based Approximator) for learnable nonlinear circuit
  Integrate this Approximator into pNNs for learnable activation function
  The training for pNNs: considering variation-aware training and learning flexibility
Conduct experiments and investigate
  the effectiveness of learnable nonlinear circuit without variation
  the effectiveness of variation-aware training with learnable nonlinear circuit
Result
  4.2% accuracy improvement
  10% - 20% accuracy improvement & 75% - 85% robustness improvement
.

## Slide 21
Learnable Nonlinear Circuitry in Printed Neuromorphics
Thank you!
Notes: So, this is my presentation. I'm very glad if there is any question or comment.

## Slide 22: Variation-aware Training
Learnable Nonlinear Circuitry in Printed Neuromorphics
Taking fabrication error/variation into account
Model the learnable parameter as stochastic variables, e.g.,
  with each element in and following a uniform distribution in this work
  , reflects printing technology
The expected loss as objective
  Monte-Carlo approximation
  build activation/negative weight functions
  in pNNs
Notes: \epsilon
Loss. Only an approximate solution through numerical methods. Monte/Carlo approximation.
objective existence

## Slide 23: Background
Learnable Nonlinear Circuitry in Printed Neuromorphics
Hardware primitive
Negative Weight Circuit
  recall: weighted-sum in crossbar
  problem: weight (conductance) is only positive
  solution: invert and still use positive conductance
    Where

## Slide 24: Integration of Approximator to pNNs
Learnable Nonlinear Circuitry in Printed Neuromorphics
  Learnable parameters for nonlinear circuits
    Inequalities: ,
  build activation/negative weight functions
  in pNNs